## Slide 1: PKI & Certificates: the technical deep dive
Book 07 — from a hardened AD CS to Cloud PKI, Entra CBA and Federal PKI
Presented by Michael F. Stratton
Not an official U.S. government publication. Independent technical analysis; not reviewed or endorsed by any federal agency.
Part 1 — Hardening and the target
Module 1 Hardening what stays · Module 2 The target PKI
Part 2 — Issuing, migrating and retiring
Module 3 Device and user certificates · Module 4 Coexistence to decommissioning
Notes: [0:00–1:04] This is the technical deep dive for Book 07 of the Federal Modernization Workbook, PKI and Certificates. It's for the PKI engineers and architects who will run the move off Active Directory Certificate Services. It comes in two parts of about twenty-five minutes each, and four modules you can watch separately. Part 1 is hardening and the target: first how to make the AD CS that stays the best-defended system you own, then the target architecture of four issuers and one lifecycle platform. Part 2 is issuing, migrating and retiring: the Intune certificate profiles, strong mapping and Entra certificate-based authentication, then coexistence, the six-wave migration, lifecycle monitoring and the decommissioning of the old CAs. The slides show tables, checklists and decision matrices. The commands live in the chapters and appendices, and the book marks them as illustrative and untested against production; I'll point you to them rather than put them on screen. Workbook: Book 07, index; Chapters 03–08; Appendices A–B.

## Slide 2: Why this matters: certificates fail at expiry, not at cutover
WHY
WHY AD CS IS THE HARDEST PART OF AD TO LEAVE
Wired into the forest
Templates, enrollment services, NTAuth, AIA and CRL objects live in the configuration partition
Cloud covers part of it
Cloud PKI issues only to Intune-managed devices; Intune doesn't manage Windows Server
DCs need certificates
Kerberos certificate trust, LDAPS and smart card logon last as long as domain controllers do
THE RULES ARE MOVING UNDER CERTIFICATES ALREADY ISSUED
Change | What the book records
Public TLS | Maximum validity 200 days from March 15, 2026 (in force), 100 days from March 15, 2027, 47 days from March 15, 2029
KB5014754 | Full Enforcement since February 11, 2025; Compatibility mode gone since September 9, 2025
Post-quantum | NIST IR 8547 draft: RSA-2048 signatures deprecated after 2030, all RSA and ECDSA disallowed after 2035
OMB M-26-15 | PQC migration plan due 120 days from June 24, 2026
Its own program: issued certificates keep working after cutover until the first expiry wave finds no issuer. The replacement issuer has to be live first, and AD CS retires last.
Sources: CA/Browser Forum Ballot SC-081v3 and Baseline Requirements 2.3.1; KB5014754; NIST IR 8547 (ipd); OMB M-26-15; Microsoft Learn — Cloud PKI, Intune platforms. Book 07, Ch 01.
Notes: [1:04–2:46] Why this matters. A certificate is a signed naming claim that has already been handed out. It sits in device stores, on smart cards, in load balancers and in trust stores nobody remembers configuring. It doesn't move when the directory moves. It keeps working until it expires, and then whatever relied on it stops. Three properties make AD CS the hardest part of Active Directory to leave. An enterprise CA is wired into the forest: its templates, enrollment services, NTAuth trust and publication points live in the configuration partition. The cloud replacements cover only part of the estate: Cloud PKI issues to Intune-managed devices, and Intune doesn't manage Windows Server. And domain controllers need certificates for as long as domain controllers exist. Meanwhile the rules are moving under certificates already issued. Public TLS maximum validity is two hundred days today, a hundred days from March 15, 2027, and forty-seven days from March 15, 2029. KB5014754 put domain controllers in Full Enforcement on February 11, 2025, and Compatibility mode has been gone since September 9, 2025. NIST's draft post-quantum transition plan proposes deprecating RSA-2048 signatures after 2030 and disallowing RSA and ECDSA signatures after 2035, and OMB M-26-15 gave agencies a hundred and twenty days from June 24, 2026 to submit a migration plan. So the move off AD CS runs as its own program. It fails at expiry, not at cutover, which can be months later and far from its cause. Workbook: Book 07, Chapter 01 — Why Certificates Outlive Every Migration.

## Slide 3: What AD CS holds up, and the four verdicts
WHAT
CHAPTER 02
Not one server
Offline standalone root; enterprise issuing CAs issue from templates stored in AD
Public Key Services: Templates, Enrollment Services, NTAuthCertificates, AIA, CDP, KRA, OID
Autoenrollment every eight hours; renewal after 80 percent of validity
Inventory four layers: CA, template, issued certificates, relying parties
Verdict | Meaning | Examples
RETIRE | The consumer is going away | EFS on migrated shares, retired SSIDs
MIGRATE | Cloud PKI through Intune, or Entra CBA, replaces it | Wi-Fi and wired 802.1X, VPN, device auth, tenant sign-in
BRIDGE | Depends on AD or a server the cloud can't reach | DCs, LDAPS, NPS and RADIUS, NTAuth trust
RETAIN | No cloud equivalent; stays on-premises | HSM code signing, network gear via SCEP
Ask in this order: retiring? then a cloud path? then dependent on AD itself? What's left is RETAIN, a short list with an owner and a review date on every entry.
Sources: Microsoft Learn — CA role service; Monitor AD CS publication health; autoenrollment renewal; Cloud PKI overview. Book 07, Ch 02; Appendix B.
Notes: [2:46–4:30] What AD CS holds up. It isn't one server. The typical estate is a two-tier hierarchy: an offline standalone root that signs the issuing CAs and its own CRL, and enterprise issuing CAs that issue from templates stored in Active Directory. Every enterprise CA also lives as objects in the forest's Public Key Services branch: certificate templates, enrollment services, the NTAuth certificates object, AIA and CDP containers, key recovery agents and OIDs. Those objects are forest-wide, which is exactly what ties AD CS to Active Directory. Domain members enroll through Group Policy autoenrollment, which runs every eight hours and renews a certificate after it passes eighty percent of its validity. Chapter 02's inventory has four layers: the CAs, the templates, the issued certificates and the relying parties. The relying-party layer decides the order of work later, because a new issuer is useful only once everything that validates it trusts it. Then every template and use case gets one of four verdicts, asked in order. RETIRE first, if the consumer is going away. MIGRATE, if Cloud PKI through Intune or Entra CBA replaces it: Wi-Fi, VPN, device authentication, tenant sign-in. BRIDGE, if it depends on AD itself or a server the cloud can't reach: domain controllers, LDAPS, NPS and NTAuth trust. RETAIN is what's left, such as HSM-held code signing, and every entry gets an owner and a review date. Appendix B applies these verdicts template by template; we'll come back to it in Module 4. Workbook: Book 07, Chapter 02 — What AD CS Holds Up; Appendix B.

## Slide 4: Module 1: Hardening what stays
Part 1 — Hardening and the target · Chapter 03
Presented by Michael F. Stratton
Not an official U.S. government publication. Independent technical analysis; not reviewed or endorsed by any federal agency.
IN THIS MODULE · ABOUT 11 MINUTES
The migration gate and the eight ESC classes as a detection checklist
CA auditing and the program's risk-scoring matrix
Baselines for retained AD CS, Cloud PKI and Entra CBA
Notes: [4:30–5:12] Module 1: hardening what stays. A migration off AD CS takes months, and for some workloads it never finishes. Throughout that time the enterprise CA keeps issuing certificates that domain controllers, VPN gateways, RADIUS servers and Entra ID accept as proof of identity. A CA can create credentials the whole environment trusts, so one over-privileged account or misconfigured setting on it can undo every other identity control. That makes hardening the first technical workstream, not a cleanup task at the end. Everything in this module is defensive: what each misconfiguration is, how to detect it, and how to fix it. Workbook: Book 07, Chapter 03 — Hardening What Stays.

## Slide 5: The gate, and where the misconfigurations live
WHAT
Template objects
ESC1–ESC4
Requester-supplied subject; Any Purpose or no EKU; enrollment agents; template ACL and owner
Defender for Identity template assessments
Public Key Services
ESC5
Write rights on NTAuthCertificates, Enrollment Services, the Templates container
No Defender for Identity assessment: ACL review and event 5136
CA configuration
ESC6, ESC7
The SAN edit flag; Manage CA and Issue and Manage Certificates
CA assessments need the sensor on the CA; events 4882, 4890, 4892
HTTP enrollment
ESC8
Web Enrollment and CES without HTTPS and Extended Protection
CA sensor assessment; IIS binding and EPA settings
The migration gate: Critical and High findings are remediated and verified before any certificate workload migrates. Under BYOCA the cloud issuer chains to this hierarchy and inherits every weakness.
Sources: SpecterOps, Certified Pre-Owned (2021; class names only); Microsoft Learn — Defender for Identity certificate assessments, posture assessments, US Government offerings. Book 07, Ch 03.
Notes: [5:12–7:01] The program carries one rule forward unchanged: misconfigurations rated Critical or High are remediated and verified before any certificate workload migrates. Migrating from a CA that can be made to issue arbitrary credentials propagates the weakness into whatever trusts the hierarchy next. And under the bring-your-own-CA model the program recommends, the new Cloud PKI issuing CA chains to the existing AD CS hierarchy, so it inherits every weakness the day it goes live. The ESC names come from SpecterOps' 2021 research; Microsoft adopted the same labels in Defender for Identity, which is why they're the shared vocabulary. The book uses them only as labels for defensive checks. The classes live in four control points. Template objects hold ESC1 through ESC4. The Public Key Services objects hold ESC5, which Defender for Identity doesn't assess, so detection is an ACL review plus directory change auditing, event 5136. The CA's own configuration holds ESC6 and ESC7, and HTTP enrollment endpoints hold ESC8. Certificate template assessments are available to every customer with AD CS; CA assessments need a Defender for Identity sensor on the AD CS server, so install it on every enterprise CA that stays. Two caveats from the book. In GCC, Defender for Identity uses the security dot microsoft dot com portal; Microsoft says new features reach GCC, GCC High and DoD within ninety days of commercial release, but preview features may not be supported there. The ESC1 and ESC6 assessments are still labeled preview, so confirm they appear in your tenant, and run the manual checks in the meantime. Workbook: Book 07, Chapter 03 — Hardening What Stays, "The migration gate" and "The ESC taxonomy."

## Slide 6: Template classes ESC1–ESC4: detect and fix
HOW
Class | The misconfiguration | How to detect it | How to fix it
ESC1 | Requester supplies the subject or SAN on a client-authentication template that broad groups can enroll in | Defender for Identity (preview); Supply in the request set; authentication EKUs; Enroll for Domain Users or similar; events 4886 and 4887 where requester and subject differ | Any one closes it: build the subject from AD, remove unneeded EKUs, restrict Enroll, require manager approval, or unpublish
ESC2 | Any Purpose or no EKU, enrollable by unprivileged users | Defender for Identity; empty or Any Purpose application policies plus an unprivileged Enroll grant | Restrict enrollment; replace Any Purpose with specific EKUs; add approval or signatures
ESC3 | A Certificate Request Agent template unprivileged users can enroll in | Defender for Identity; inventory agent templates and issued agent certificates; test restrictions with an allowed and a disallowed request | Remove the EKU or broad enrollment, require approval, unpublish, or set CA enrollment agent restrictions
ESC4 | Unprivileged write rights on, or ownership of, a template | Defender for Identity (ACL and owner); Security tab; event 5136, with Audit Directory Service Changes and a SACL | Remove the ACEs; privileged, monitored owner; keep the CA computer account's Read
Sources: Microsoft Learn — Defender for Identity certificate assessments; certenroll.h name flags; Audit Certification Services; Manage AD CS certificate templates; Secure, delegate and audit CA administration. Book 07, Ch 03.
Notes: [7:01–8:55] The template classes, as a checklist. ESC1: a template lets the requester supply the subject or subject alternative name, permits client authentication, and broad unprivileged groups can enroll, so a member could obtain a certificate that names someone else. Detect it with Defender for Identity, and by hand: Supply in the request on the Subject Name tab, an authentication purpose such as Client Authentication, Smart Card Logon, PKINIT or Any Purpose, and Enroll granted to Authenticated Users, Domain Users, Domain Computers or Everyone. On the CA, events 4886 and 4887 show requests where the requester and the issued subject differ. Any one remediation closes it: build the subject from Active Directory, remove authentication EKUs the template doesn't need, restrict Enroll, require CA certificate manager approval, or take the template off every CA if it's unused. ESC2 is Any Purpose or no EKU on a broadly enrollable template. A no-EKU template restricted to PKI administrators, such as a subordinate CA template, isn't the same exposure. ESC3 is a broadly enrollable enrollment agent template. Treat an enrollment agent certificate as an impersonation capability. Microsoft doesn't publish a Windows Server 2025 procedure for enrollment agent restrictions, so validate the existing configuration in a lab first. ESC4 is write rights or ownership on a template held by anyone but the PKI administrators. Changes are logged as event 5136 only when directory change auditing is on and the objects carry a matching SACL. One trap when you fix it: if you remove Authenticated Users from a template ACL, grant each issuing CA's computer account Read, or the CA can no longer read the template. Workbook: Book 07, Chapter 03 — Hardening What Stays, ESC1–ESC4.

## Slide 7: Directory and CA classes ESC5–ESC8, then ESC11 and ESC15
HOW
Class | The misconfiguration | How to detect it | How to fix it
ESC5 | Unprivileged write on Public Key Services objects such as NTAuthCertificates or Enrollment Services | No Defender for Identity assessment: review the container ACLs; compare the NTAuth store with the approved CA list; SACL plus event 5136 | Limit write to Enterprise Admins and the CA computer accounts; alert on NTAuth changes; never delete a flagged object without a dependency check
ESC6 | The CA-wide EDITF_ATTRIBUTESUBJECTALTNAME2 flag lets any requester supply SANs on any template | Defender for Identity CA assessment (sensor; preview); read the policy module's edit flags | Find out why it was set, clear it, restart the service
ESC7 | Unprivileged Manage CA or Issue and Manage Certificates on the CA | Defender for Identity (sensor); baseline the CA's Security tab; alert on 4882, 4890 and 4892 | Remove from unprivileged groups; separate role groups of named accounts, each with an owner and review date
ESC8 | Web Enrollment or CES accepts NTLM without HTTPS or Extended Protection | Defender for Identity (sensor) and its issuance alert; inventory IIS: HTTP binding, Require SSL, EPA | EPA Required; Require SSL; restart IIS; restrict NTLM; remove Web Enrollment nothing needs
Also on the checklist: ESC11, RPC enrollment without packet privacy (turn the encryption flag back on); ESC15, templates on CAs unpatched for CVE-2024-49019 (remove unprivileged enrollment, turn off Supply in the request, patch).
Sources: Microsoft Learn — Defender for Identity certificate assessments and alerts; Monitor AD CS publication health; certutil; KB5014754; KB5005413 (NTLM relay on AD CS). Book 07, Ch 03.
Notes: [8:55–10:44] The directory and CA classes. ESC5 is unprivileged write access on the forest's Public Key Services objects. The NTAuth certificates object holds the CAs trusted to issue logon and domain controller certificates, and each enrollment services object records what a CA can issue and who can enroll. Write access to either is control over authentication. Defender for Identity has no ESC5 assessment, so review the ACLs, compare the NTAuth store with your approved CA list, and audit changes through event 5136. ESC6 is the CA-wide flag that lets any requester supply subject alternative names on any template. Find out why it was turned on, since some old workflows depended on it, then clear it and restart the service. The book corrects a common belief here: KB5014754 introduced strong mapping, which reduces what a forged name can do against Kerberos, but it doesn't change what the CA will sign, and other relying parties may still trust the name. Clear the flag regardless. ESC7 is unprivileged Manage CA or Issue and Manage Certificates. Build separate groups for CA administrators, certificate managers, enrollment agents, auditors and backup custodians. Service accounts count too: the Intune Certificate Connector and lifecycle tooling both hold Issue and Manage Certificates, so each is a certificate manager in all but name. ESC8 is an HTTP enrollment endpoint that accepts NTLM without HTTPS or Extended Protection. Microsoft's advisory: Extended Protection set to Required, Require SSL, restart IIS, and restrict NTLM where you can. Better still, remove Web Enrollment wherever nothing depends on it, and apply the same rules to NDES. Workbook: Book 07, Chapter 03 — Hardening What Stays, ESC5–ESC8 and "Beyond ESC8."

## Slide 8: Turn on CA auditing, then watch the baseline events
HOW
TWO SETTINGS, NEITHER WORKS ALONE
AD CS logs nothing by default
GPO on the CA servers: Audit Certification Services, Success and Failure
CA audit filter: all categories, then restart in a maintenance window
Full auditing can slow restarts on a large database: test it
Forward by WEF to the SIEM; size the Security log to outlast an outage
Generate each event in a test before writing the rule
Event | Meaning | Why the program watches it
4886 | Request received | Volume and requester, per template
4887 | Request approved, certificate issued | Every credential; retired templates
4888 | Request denied | Probing of restricted templates
4870 | Certificate revoked | Leaver and incident evidence
4882 | CA security permissions changed | ESC7 drift
4885 | Audit filter changed | Auditing turned down
4890 | Certificate manager settings changed | ESC7 drift
4892 | A CA property changed | ESC6 and configuration drift
4896 | Rows deleted from the database | Evidence destruction
4897 | Role separation enabled | Role model change
Sources: Microsoft Learn — Secure, delegate and audit CA administration; Audit Certification Services; Defender for Identity event auditing on AD CS. Book 07, Ch 03.
Notes: [10:44–12:25] Every detection in this module depends on evidence, and AD CS produces none by default. Two settings are needed, and neither works without the other. The CA's audit filter selects which CA operations are audited. The Audit Certification Services advanced audit subcategory lets the operating system generate the events. Set the subcategory to Success and Failure in a dedicated GPO linked to the CA servers, set the audit filter to cover every category, and restart the service in a maintenance window. Full auditing includes the start and stop category, which can slow restarts on a CA with a large database, so test that first. Then watch Microsoft's focused baseline. 4886, 4887 and 4888 are requests received, issued and denied: issuance volume per template, every credential issued, and probing of templates that should be restricted. 4870 is revocation evidence. 4882 and 4890 are permission and certificate manager changes, which is ESC7 drift. 4885 is someone changing the audit filter. 4892 is a CA property change, which catches the ESC6 flag. 4896 is rows deleted from the CA database. 4897 is role separation enabled. Microsoft recommends generating each event in a nonproduction test before writing the collection rule, so an assumed event doesn't become a blind spot. Forward through Windows Event Forwarding to a collector and the SIEM. Forwarding doesn't stop a full local log from overwriting evidence, so size the CA's Security log for the longest plausible collection outage. Workbook: Book 07, Chapter 03 — Hardening What Stays, "Turn on CA auditing."

## Slide 9: The risk-scoring matrix, and what closed means
WHO
Class | Misconfiguration | Risk | Domain compromise? | Priority | Defender for Identity
ESC1 | Requester supplies subject on an authentication template | Critical | Yes | Immediate | Template; preview
ESC2 | Any Purpose or no EKU, broadly enrollable | Critical | Possible | Immediate | Template
ESC3 | Enrollment agent template broadly enrollable | High | Possible | Within 2 weeks | Template
ESC4 | Writable template ACL or unprivileged owner | High | Possible | Within 2 weeks | Template
ESC5 | Writable Public Key Services objects | High | Possible | Within 2 weeks | No; manual, 5136
ESC6 | EDITF_ATTRIBUTESUBJECTALTNAME2 on | Critical | Yes | Immediate | CA sensor; preview
ESC7 | Unprivileged Manage CA or Issue and Manage | High | Possible | Within 2 weeks | CA sensor
ESC8 | HTTP enrollment without HTTPS and EPA | Critical | Yes | Immediate | CA sensor
Every row blocks migration until verified closed: Defender for Identity shows no exposed entities (allow its 24-hour update lag), plus a manual re-check for ESC5. Ratings are the program's own scoring.
Sources: Microsoft Learn — Defender for Identity certificate assessments; posture assessments. Risk, compromise and priority columns are program scoring. Book 07, Ch 03.
Notes: [12:25–13:49] The program scores each class for prioritization. Be clear about what's whose. The risk level, domain-compromise and priority columns are the program's own scoring, carried forward from its PKI guide. The detection column is from Microsoft's documentation. Four classes are Critical with Immediate priority: ESC1, ESC2, ESC6 and ESC8. Four are High, to be fixed within two weeks: ESC3, ESC4, ESC5 and ESC7. One change from the original guide: ESC2 is downgraded from Yes to Possible for domain compromise, because Microsoft describes its main effect as undermining trust in other certificate consumers rather than direct user impersonation. Immediate means the finding is fixed, or the template or endpoint is taken out of service, before the next change window closes. And every row is a migration blocker until it's verified closed. Verified has a definition: the Defender for Identity assessment shows no exposed entities, remembering that scores and statuses update every twenty-four hours, plus a manual re-check for ESC5, which Defender for Identity doesn't assess. That's the record the gate reads. Chapter 07's first wave doesn't exit until every Critical and High finding is remediated and re-tested, and the PKI owner and the security team have approved the assessment. Workbook: Book 07, Chapter 03 — Hardening What Stays, "The risk-scoring matrix"; Chapter 07, Wave 1.

## Slide 10: Hardening baselines: retained AD CS, Cloud PKI and Entra CBA
HOW
THE AD CS THAT REMAINS
Tier 0 until it's gone
Unpublish every template no BRIDGE or RETAIN workload needs
Keep CRLs on schedule; test with -urlfetch from client networks
Backup-CARoleService before every change
Hardened management host; RPC only from endpoints that need it
FIPS-validated HSM keys, non-exportable; dual control for the root
MICROSOFT CLOUD PKI
A new admin surface
Custom Intune roles and scope tags; no built-in PKI admin role
EKUs fixed at creation; no Any Purpose
Windows keys in the TPM KSP, otherwise fail: 2048-bit RSA
One-year validity for authentication certificates
No production CAs during a trial: trial keys stay in software
ENTRA CBA
What it trusts and binds
High-affinity bindings required in production
Custom strength: named issuers or policy OIDs, up to five each
Require CRL validation; one HTTP CRL per CA; no OCSP
CRL at least every 24 hours (program rule)
CA scoping, GA since April 2026: one group per CA, 30 rules; pilot it
Sources: Microsoft Learn — Secure, delegate and audit CA administration; Cloud PKI overview and configure CA; SCEP profiles; Entra CBA technical concepts, CRL, authentication strengths; Entra what's new. Book 07, Ch 03.
Notes: [13:49–15:43] Three baselines close the module. The AD CS that remains keeps running for months or years for BRIDGE and RETAIN workloads. Remove every template those workloads don't need from each CA's issuance list; it's reversible. Alert on requests for templates that should no longer be requested. Keep CRL publication on schedule, and test it from representative client networks. Back up the CA before every change. Treat CA servers as Tier 0, the program's designation, because the CA can mint domain authentication credentials. And the program requires FIPS 140-2 or 140-3 validated modules, CA keys held non-exportable in an HSM, and dual control for root ceremonies. Cloud PKI removes most of that attack surface but adds its own. Scope administrators with custom Intune roles and scope tags; there's no built-in Intune PKI Administrator role. EKUs are fixed at creation. On Windows, set the key storage provider to TPM, otherwise fail; a 4096-bit key can only live in the software provider, so the program uses 2048-bit RSA in the TPM. The program sets one-year validity. And don't build production CAs during a trial. Entra CBA is a relying party, so its hardening is about trust and binding. Require high-affinity bindings in production. Use a custom authentication strength that names issuers or policy OIDs, up to five of each, for sensitive resources. Require CRL validation; the program wants each trusted issuing CA to publish a CRL at least every twenty-four hours, because Entra caches it. And CA scoping, generally available since April 2026, ties each CA to one group, with up to thirty rules. A mistake can lock users out, so pilot it. Workbook: Book 07, Chapter 03 — Hardening What Stays, "Hardening the AD CS that remains," "Hardening Microsoft Cloud PKI," "Hardening Entra certificate-based authentication."

## Slide 11: Module 2: The target PKI
Part 1 — Hardening and the target · Chapter 04
Presented by Michael F. Stratton
Not an official U.S. government publication. Independent technical analysis; not reviewed or endorsed by any federal agency.
IN THIS MODULE · ABOUT 10 MINUTES
What Microsoft Cloud PKI can and can't issue
Cloud root or bring-your-own-CA, and the program's choice
Retained AD CS, Federal PKI for PIV, and one lifecycle platform
Notes: [15:43–16:30] Module 2: the target PKI. The guide this book replaces said Microsoft Cloud PKI eliminates the need for on-premises AD CS for most certificate use cases. That's true for devices and wrong for the estate. There's no single replacement for AD CS. The target is four issuers, each chosen for the subjects only it can serve: Cloud PKI for Intune-managed devices, a smaller and hardened AD CS for what still depends on Active Directory, the Federal PKI for PIV, and public CAs for names the internet must trust. Entra ID sits beside all of them as a relying party, not an issuer. One root-of-trust decision and one lifecycle platform hold them together. Workbook: Book 07, Chapter 04 — The Target PKI: Cloud PKI, AD CS and Federal PKI.

## Slide 12: Microsoft Cloud PKI: what it can and can't issue
WHAT
Cloud PKI can | Cloud PKI can't
Issue leaf certificates to Intune MDM-enrolled Android, iOS/iPadOS, macOS and Windows devices | Issue to anything not enrolled in Intune: no domain controller, NPS, web or SQL Server certificate
Issue user and device client-authentication certificates for Wi-Fi, VPN and CBA | Issue the TLS server certificates RADIUS, Wi-Fi infrastructure and VPN gateways present
Issue through SCEP, renew and revoke; RSA 2048, 3072 or 4096; SHA-256, 384 or 512 | Issue through PKCS or imported PKCS profiles
Publish a CRL per CA: valid seven days, republished every 3.5 days and on each revocation | Answer OCSP, or offer data residency
Host up to three CAs per tenant: root, issuing and BYOCA issuing all count | Change a CA's EKUs after creation: a new EKU means a new CA
Keys
Licensed CAs: Azure Managed HSM, no subscription of your own. Trial CAs: software keys, never converted
Licensing
Add-on to Intune Plan 1 or 2. M365 E5 and E7 include it for commercial customers from July 2026; confirm Government entitlement
Clouds
GCC uses the commercial Intune service. GCC High from the week of Sept. 28, 2026. Not supported in DoD
Sources: Microsoft Learn — Cloud PKI overview, fundamentals, deployment models, configure CA; Intune supported platforms; Intune add-ons, planning guide, what's new (2606, 2609); Intune GCC High and DoD. Book 07, Ch 04.
Notes: [16:30–18:21] Cloud PKI is a Microsoft-hosted PKI managed in the Intune admin center. It hosts the root and issuing CAs, a SCEP registration authority for each issuing CA, the CRL distribution point and the AIA endpoint, which together replace the on-premises CA, NDES server and Certificate Connector for device certificates. What it can do. Issue client-authentication certificates to Intune-enrolled Android, Apple and Windows devices, through SCEP. Publish a CRL per CA, valid seven days, republished every three and a half days and on every revocation. And host up to three CAs per tenant. What it can't. Issue to anything not enrolled in Intune; Intune doesn't support Windows Server, so no domain controller, NPS server, web server or SQL Server gets a Cloud PKI certificate. Issue the server certificates RADIUS and VPN gateways present; Microsoft says those must come from another CA. Issue through PKCS. Answer OCSP. And change a CA's EKUs after creation. Plan the three-CA count before you create anything. Keys: licensed CAs use Azure Managed HSM; trial CAs use software keys that can't be converted after purchase. Licensing: Cloud PKI is a subscription on top of Intune Plan 1 or 2. From July 2026, Microsoft 365 E5 and E7 include it for commercial customers; Microsoft says Government plans are planned to align, subject to compliance and regulatory requirements, so confirm the entitlement on the current SKU. And availability: GCC uses the commercial Intune service, so availability follows it and licensing is the question. Cloud PKI became available in GCC High in the week of September 28, 2026, and isn't supported in DoD. Workbook: Book 07, Chapter 04 — The Target PKI, "Microsoft Cloud PKI."

## Slide 13: Two ways to anchor trust: a cloud root or bring-your-own-CA
WHAT
OPTION 1
Cloud PKI root CA
Two-tier hierarchy, private to the tenant
Root 5–25 years, issuing CA 2–10 years in the admin center; Graph allows custom periods
Root key Microsoft-managed in Azure Managed HSM
Every relying party has to be given the new root
OPTION 2
Bring your own CA (BYOCA)
Intune makes the request; a private CA at any tier signs it with the Subordinate CA template
The signer sets validity and hash; your key size caps the SCEP profiles; no 1024-bit or SHA-1
AIA comes from your CA, and AD CS defaults to LDAP: set an HTTP AIA first
Relying parties keep the chain, but also get the BYOCA issuing CA; Android needs the full chain
The root CRL becomes production: under BYOCA every relying party, Entra ID included, must still fetch the private root's CRL. Entra accepts one HTTP CRL per CA and fails sign-in if it can't reach it.
Sources: Microsoft Learn — Cloud PKI deployment models; configure CA; configure BYOCA; renew a CA; Entra CBA overview and CRL. Book 07, Ch 04.
Notes: [18:21–20:20] Cloud PKI offers two ways to anchor trust, and both can coexist in one tenant. The Cloud PKI root CA: you create a root and one or more issuing CAs in the cloud. It's a two-tier hierarchy. In the admin center the root's validity is five to twenty-five years and an issuing CA's is two to ten, never longer than its root; the Graph API allows custom periods. The catch is that every relying party has to be given the new root. Bring your own CA: you create an issuing CA in the cloud, Intune generates a certificate signing request, and your private CA signs it. Four details matter. The signer doesn't have to be the root; Microsoft says it can be a root or issuing CA from any tier, using the Subordinate Certification Authority template. The signer sets the terms: validity and hash algorithm come from the signing CA, the key size you choose caps the SCEP profiles that use it, and 1024-bit keys and SHA-1 aren't supported. The AIA comes from your CA, and AD CS defaults to an LDAP location, so configure an HTTP AIA before signing; Android doesn't follow AIA paths, so deploy the full chain there. And relying parties still get one new certificate: Microsoft recommends deploying the BYOCA issuing CA certificate to them, because AIA retrieval isn't guaranteed on every platform. Renewal repeats the signing. One consequence matters more than any of these. Under BYOCA the private root CRL stays where it is, and every relying party, Entra ID included, must still fetch it. An offline root that publishes its CRL only over LDAP, or late, breaks the cloud issuer as surely as the on-premises one. Workbook: Book 07, Chapter 04 — The Target PKI, "Two deployment models" and "What BYOCA actually requires."

## Slide 14: The deployment-model decision, and the program's choice
WHO
Criterion | Cloud PKI root CA | BYOCA
Existing private PKI | Not required | Required: a CA at any tier signs
Trust chain | New chain to every relying party | Existing chain, plus the BYOCA issuing CA
Root key custody | Microsoft-managed HSM | Wherever the AD CS root key is held
Ongoing on-premises dependency | None | Private root CRL reachable over HTTP
CA count (of three) | Two for a minimal hierarchy | One per BYOCA issuing CA
DC, LDAPS and server certificates | Can't serve | Can't serve
Rollback | Revert devices to AD CS and redistribute trust | Simpler: the original root and issuing CAs keep running
PROGRAM RECOMMENDATION
BYOCA, with three rules
Harden first: the root's hierarchy passes the Chapter 03 gate before it signs
Sign with the offline root at a key ceremony, so the cloud CA is a peer of the AD CS issuing CAs
Treat the root CRL as production: internet-reachable HTTP, monitored, next ceremony dated
Building PKI for the first time, cloud-first? A Cloud PKI root removes every on-premises dependency
Sources: Microsoft Learn — Cloud PKI deployment models; configure BYOCA; renew a CA; Entra CBA overview. Criteria and recommendation are the program's assessment. Book 07, Ch 04.
Notes: [20:20–22:05] A Cloud PKI root needs no existing private PKI, brings a new chain that has to reach every relying party and every forest, and keeps the root key in a Microsoft-managed HSM. BYOCA needs a private CA to sign, preserves the chain relying parties already hold, keeps root custody wherever your AD CS root key is, and adds one ongoing on-premises dependency: the private root's CRL must stay published and reachable over HTTP. Neither model can serve domain controller, LDAPS or server certificates, because Cloud PKI issues only to Intune-enrolled devices. And rollback is simpler under BYOCA, because the original root and its issuing CAs keep running. The program's recommendation, for an organization with an established AD CS hierarchy, an offline root and cross-forest trust, is BYOCA. It preserves the trust chain, needs one cloud CA rather than two, and keeps a natural rollback path. For an organization building PKI for the first time alongside cloud-first identity, a Cloud PKI root removes every on-premises dependency. Three program rules go with BYOCA. Harden first: the root's hierarchy passes the Chapter 03 gate before it signs a cloud issuing CA. Sign with the root, not an AD CS issuing CA, so the cloud issuer is a peer of the existing issuing CAs and retiring them later doesn't touch it. And treat the root CRL as production: publish it to an internet-reachable HTTP location on a schedule with margin, monitor it, and record the next ceremony date before the current CRL expires. Workbook: Book 07, Chapter 04 — The Target PKI, "The deployment-model decision matrix" and "The program's recommendation."

## Slide 15: What AD CS is kept for, and who issues server certificates
WHAT
Kept for | Ends when
Domain controller and KDC certificates | The last domain controller retires
LDAPS | LDAP-bound applications move
NPS, RADIUS and VPN gateway server certificates | RADIUS moves; until then, the server issuer decision
Internal server TLS, including SQL Server | See the issuer decision
Network equipment through NDES | Devices replaced or another path approved
HSM-held code signing | The signing requirement ends
S/MIME issuance and key history | Mail encryption moves and old keys aren't needed
THE SERVER ISSUER DECISION
Same chain, automated renewal
Internal names: retained AD CS, requested and renewed through CyberArk Certificate Manager
Internet names: a public CA, also through the CLM platform
After AD: a standalone AD CS issuing CA under the same root; template policy moves into the CLM platform
Every retained CA stays under the Chapter 03 baseline
Sources: Microsoft Learn — Cloud PKI fundamentals and deployment models; smart card logon with third-party CAs; manage templates; CyberArk — Microsoft CA (enterprise and standalone) driver. Book 07, Ch 04.
Notes: [22:05–24:05] Chapter 04 records what AD CS is kept for and when each use ends. Domain controller and KDC certificates stay until the last domain controller retires: servers can't get Cloud PKI certificates, and smart card or certificate logon to the domain needs a domain controller certificate chaining to a CA in the forest's NTAuth store. LDAPS stays until LDAP-bound applications move. NPS, RADIUS and VPN gateway server certificates stay until RADIUS moves, and until then they fall under the server issuer decision. Network equipment through NDES and HSM-held code signing stay too. And S/MIME: delivery can move to Intune imported PKCS, but the issuer and its key history stay. That leaves internal server TLS, which Chapter 02 parked as BRIDGE until an issuer was named. The program's decision has three parts. Internal names are issued by the retained AD CS hierarchy, but requested and renewed through CyberArk Certificate Manager rather than by hand or by server autoenrollment, so every server certificate has an owner, an expiry alert and automated renewal in one place. That covers NPS and RADIUS servers, VPN and Remote Desktop gateways and SQL Server as well as web servers. Domain controller certificates, which also serve LDAPS, stay on autoenrollment. Names the internet must trust come from a public CA, also through the lifecycle platform, because public lifetimes are on the shrinking schedule. And after Active Directory: enterprise CAs need AD, and standalone CAs don't use templates. When the forest retires, server issuance moves to a standalone AD CS issuing CA under the same root, still driven by the lifecycle platform, which supports both kinds of Microsoft CA. That keeps server certificates on the existing chain with no new root to distribute. Workbook: Book 07, Chapter 04 — The Target PKI, "AD CS, retained for what only it can do" and "The issuer decision for internal server certificates."

## Slide 16: Federal PKI for PIV, and one lifecycle platform
WHO
FEDERAL PKI
For PIV: trust, don't issue
Shared service providers issue PIV under the Federal Common Policy; FIPS 201-3 sets the standard
FCPCAG2 isn't in Microsoft, Mozilla or Apple stores: deploy it by Intune profile and GPO
Domain smart card logon: issuing CA in NTAuth, a certificate on every DC
Upload the chain to Entra ID; CBA validates, it doesn't issue
Issuer | Who manages the lifecycle
Cloud PKI | Intune issues, renews and revokes; the CLM platform reads its inventory
AD CS (retained) | The CLM platform, through its Microsoft CA integration (enterprise and standalone)
Public CAs | The CLM platform
Federal PKI (PIV) | The card management system and the credentialing office
CyberArk Certificate Manager, Self-Hosted: its CA account holds Issue and Manage Certificates, so it's in the ESC7 review. The SaaS edition had no FedRAMP listing on Oct. 20, 2026, so it runs inside the program's boundary.
Sources: GSA IDManagement.gov, FPKI 101; NIST FIPS 201-3; Microsoft Learn — third-party smart card logon; CyberArk — Microsoft CA driver; Palo Alto Networks; FedRAMP Marketplace dataset (Oct. 20, 2026). Book 07, Ch 04.
Notes: [24:05–26:00] PIV certificates aren't issued by Cloud PKI or by the program's AD CS, and the migration doesn't change their issuer. The Federal PKI's root for the federal government is the Federal Common Policy CA G2, and shared service providers are contracted to issue the certificates on PIV cards. What the target PKI has to do for PIV is trust, not issue. Distribute the federal root, because it isn't in the Microsoft, Mozilla or Apple trust stores by default: an Intune trusted certificate profile for managed devices, Group Policy for domain members. Keep NTAuth right while the domain exists, because smart card logon with certificates from a non-Microsoft CA needs that issuing CA in NTAuth, and a certificate on every authenticating domain controller. And upload the chain to Entra ID, which validates PIV certificates against its trust store. Then lifecycle. Cloud PKI and Intune issue, renew and revoke what they put on managed devices. Everything else is the lifecycle platform's job, and for this program it's CyberArk Certificate Manager, now part of Palo Alto Networks, from the program's existing machine-identity vendor; the program doesn't add a second lifecycle vendor. Two facts shape how it's deployed. Its CA account is privileged: to enroll through a Microsoft CA it holds Read, Issue and Manage Certificates, and Request Certificates, so it falls under the ESC7 review. And in the FedRAMP Marketplace dataset as of October 20, 2026, none of Palo Alto Networks' authorized packages is Certificate Manager or Next-Generation Trust Security. Until one is, the program deploys Certificate Manager, Self-Hosted inside its own authorization boundary. That's a program decision, to revisit when the Marketplace changes. Workbook: Book 07, Chapter 04 — The Target PKI, "Federal PKI for PIV" and "Certificate lifecycle management."

## Slide 17: Module 3: Device and user certificates
Part 2 — Issuing, migrating and retiring · Chapter 06
Presented by Michael F. Stratton
Not an official U.S. government publication. Independent technical analysis; not reviewed or endorsed by any federal agency.
IN THIS MODULE · ABOUT 12 MINUTES
Intune trusted certificate, SCEP and PKCS profiles
Strong certificate mapping under KB5014754
Entra CBA: trust, bindings, factors and staged rollout
Notes: [26:00–26:52] Module 3: device and user certificates. Intune puts certificates on devices. Entra ID decides whether a certificate proves who someone is. Those are two jobs, and each one fails differently. When Intune delivery fails, a device has no certificate and Wi-Fi, VPN or an application refuses it. The failure is local and visible in the profile report. When Entra certificate-based authentication goes wrong, the danger is the opposite: a certificate that should fail might pass, because the trust store holds too much, revocation isn't configured, or a binding is weak. Keep the two jobs apart in planning. They meet at one point, a user certificate delivered by Intune and then used to sign in, and that's where most migration surprises come from. Workbook: Book 07, Chapter 06 — Device and User Certificates: Intune and Entra CBA, "Two jobs, two failure modes."

## Slide 18: Three delivery paths, one trusted certificate profile first
HOW
Deploy first — trusted certificate profile: root and issuing CA certificates as DER .cer, one profile per platform; for BYOCA, every CA in the private chain plus the BYOCA issuing CA. No trusted root, no SCEP or PKCS.
SCEP with Cloud PKI
Device makes the key and request; the Cloud PKI registration authority checks the Intune challenge; the issuing CA signs. No on-premises servers. Don't mix NDES and Cloud PKI URLs in one profile.
SCEP with AD CS
NDES is the registration authority; the Certificate Connector adds the policy module that checks the challenge. The key stays on the device.
PKCS with AD CS
The connector generates the key on its own server and returns a PFX; the template must allow export. Program preference: SCEP wherever either fits.
Why SCEP is safe on the internet: Intune wraps each request in an encrypted, signed challenge, and the registration authority rejects any subject or SAN that doesn't match what Intune expected.
Sources: Microsoft Learn — trusted root profiles; Cloud PKI overview; configure BYOCA; SCEP infrastructure; PKCS profiles. Book 07, Ch 06.
Notes: [26:52–28:40] Every other profile depends on the trusted certificate profile. It deploys the public certificate of the root and of intermediate or issuing CAs, so the device can build the chain. Export each CA certificate as a DER-encoded file, never the private key, and create one profile per platform. With Cloud PKI, that's the Cloud PKI root and issuing CAs. With BYOCA, it's every CA in the private hierarchy as well as the BYOCA issuing CA, on every platform. If a device doesn't trust the root, the SCEP or PKCS profile fails. Then three paths. SCEP with Cloud PKI: the device generates its own key pair and request; the old guide said Intune generates it, and it doesn't. The Cloud PKI registration authority checks the request against the Intune challenge, and the issuing CA signs. No on-premises CA, NDES server or connector. Don't mix NDES and Cloud PKI SCEP URLs in one profile. SCEP with AD CS runs through two pieces of on-premises software: NDES as the registration authority, and the Certificate Connector, which adds the Intune policy module. The private key still never leaves the device. PKCS doesn't use NDES. The connector generates the key pair on its own server, requests the certificate, and hands the certificate and key to Intune as a PFX. So the template must allow export, and the private key exists, however briefly, somewhere other than the device that uses it. That's the trade PKCS makes for not needing NDES, and it's why the program prefers SCEP wherever a use case allows either. Workbook: Book 07, Chapter 06 — Device and User Certificates, "The trusted certificate profile comes first," "SCEP profiles," "PKCS and imported PKCS profiles."

## Slide 19: NDES and the connector, and which profile for which use
HOW
AD CS THROUGH NDES
Strict infrastructure rules
Enterprise CA only; NDES server domain-joined, same forest, not a DC, not the CA
Reverse proxy with passthrough preauthentication
SCEP template: subject in the request, Enroll for the NDES account only
Connector holds Issue and Manage Certificates: CA administrative tier
Three templates per NDES server; no clustering; RA certificates expire
Connector 6.2510.3.3007 (May 18, 2026) is current; let it auto-update
Use case | Profile | Issuer
Wi-Fi 802.1X, device or user | Trusted + SCEP | Cloud PKI
VPN client authentication | Trusted + SCEP | Cloud PKI, or AD CS via NDES
Web application mTLS client | Trusted + SCEP | Cloud PKI
User certificate for Entra CBA | Trusted + SCEP | Cloud PKI or AD CS
S/MIME signing | PKCS | AD CS or existing CA
S/MIME encryption | Imported PKCS | Existing CA with key archival
Certificate logon to AD | SCEP or PKCS with the SID | AD CS, or a CA in NTAuth
Sources: Microsoft Learn — SCEP infrastructure; Entra joined on-premises SSO with certificates; NDES enrollment agent renewal; Certificate Connector overview; PKCS profiles; Entra join planning. Book 07, Ch 06.
Notes: [28:40–30:34] When the issuer is AD CS, the infrastructure rules are strict. The CA must be an enterprise CA; a standalone CA isn't supported. The NDES and connector server is domain-joined in the same forest, and is neither a domain controller nor the issuing CA. Publishing NDES to the internet needs a reverse proxy with passthrough preauthentication. The SCEP template supplies the subject in the request, which is exactly the setting Chapter 03 treats as dangerous; here the policy module enforces the subject, so the template is safe only while Enroll is limited to the NDES service account. Audit that ACL like any other. And the connector's Issue and Manage Certificates right is a CA officer right, so the connector server belongs in the CA's administrative tier. NDES picks a template by the request's purpose, so one server serves at most three templates. It can't be clustered; for availability, run several identical servers. Its own two registration-authority certificates expire like any other and are a frequent cause of outages. Keep the connector current. The current release is 6.2510.3.3007, from May 18, 2026. Let it update itself and alert on Warning or Error. Which profile for which use. Wi-Fi, VPN, web application client certificates and user certificates for Entra CBA are trusted plus SCEP, from Cloud PKI, or from AD CS while a relying party trusts only AD CS. S/MIME signing is PKCS; S/MIME encryption is imported PKCS from a CA with key archival, because old mail needs the old keys. And a user certificate for certificate logon to AD needs the SID added, from AD CS or a CA in NTAuth. Workbook: Book 07, Chapter 06 — Device and User Certificates, "SCEP with AD CS through NDES," "Keep the connector current," "Which profile for which use."

## Slide 20: Strong certificate mapping: Full Enforcement is the present
WHAT
Date | KB5014754 phase
May 10, 2022 | Compatibility mode: strong preferred, weak allowed with warnings
April 11, 2023 | The Disabled setting is ignored
Feb. 11, 2025 | Full Enforcement where no value is set; Compatibility still selectable
Sept. 9, 2025 | Registry key no longer honored; no way back
KDC event | Meaning (2008-era DCs log 41, 48, 49)
39 | No strong mapping found
40 | Certificate predates the account; no strong mapping
41 | SID extension doesn't match the account's SID
WHAT INTUNE PROFILES NEED
Strong from day one
Strong forms: the SID extension, the SID in a SAN URL, or IssuerSerialNumber, SKI or SHA1PublicKey on the account
SCEP: SAN URI attribute {{OnPremisesSecurityIdentifier}}; Cloud PKI too
PKCS: current connector with EnableSidSecurityExtension = 1
User certificates on all platforms; device certificates only on hybrid joined Windows
Logon CAs must be in NTAuth; pilot with a new profile, because editing one revokes
Sources: Microsoft Support — KB5014754 (phases; Kdcsvc events 39–41, and 41/48/49 on Server 2008 and 2008 R2); Microsoft Learn — SCEP and PKCS profiles; third-party smart card logon; remove certificates. Book 07, Ch 06.
Notes: [30:34–32:32] Before May 2022, a domain controller mapped a certificate to an account by name. KB5014754 changed the KDC to want a strong mapping. The old guide said enforcement began in February 2025; that was one step of four. May 2022, Compatibility mode. April 2023, the Disabled setting is ignored. February 11, 2025, Full Enforcement for domain controllers with no value set. September 9, 2025, the registry key is no longer honored. As of October 2026, every current domain controller is in Full Enforcement with no supported way back. A strong mapping is the SID extension AD CS adds, the SID in a tagged SAN URL, which is Intune's form, or an explicit strong value on the account, such as issuer and serial number, SKI or SHA-1 public key. What Intune profiles need. It applies to user certificates on all platforms and to device certificates only on hybrid joined Windows devices, and the user or device must be synced from AD. For SCEP, add a SAN attribute of type URI with the on-premises security identifier variable. The old guide said Cloud PKI adds it automatically; Microsoft's instructions say you must add it. For PKCS, run the current connector and set the SID security extension registry value. Logon certificates need their issuing CA in NTAuth. Pilot with a new profile, because editing a SCEP profile revokes what it issued. To find weak certificates, sweep the KDC's System log for events 39, 40 and 41. One trap on a mixed estate: on Server 2008 and 2008 R2, event 41 means no strong mapping, and the other two are logged as 48 and 49. Read the event text before you classify a hit. Workbook: Book 07, Chapter 06 — Device and User Certificates, "Strong certificate mapping (KB5014754)."

## Slide 21: Entra CBA: the sign-in, the trust store and revocation
HOW
1 Username
Home realm discovery; Use a certificate or smart card
2 mTLS
certauth endpoint requests the client certificate
3 Validate
Chain against the trust store; CRL checked
4 Bind
Username bindings find exactly one user
5 Factor
Single- or multifactor, against Conditional Access
TRUST STORE
Upload every CA in the user-certificate chain to the PKI-based store: 250 CAs, 8 KB each
Privileged Authentication Administrator; bulk .p7b upload needs P1 or P2
Every CA you add can authenticate any user it can be bound to
REVOCATION
One CRL per CA, internet HTTP or HTTPS (HTTP recommended); no OCSP, no LDAP
Downloaded in 10 seconds; 20 MB commercial and GCC, 45 MB Azure Government
Cached until next update: revoke sessions for an immediate cutoff
Sources: Microsoft Learn — Entra CBA technical concepts; set up Entra CBA; Entra CBA CRL; What is Entra CBA (unsupported scenarios). Book 07, Ch 06.
Notes: [32:32–34:30] How a CBA sign-in works, as Microsoft documents it. The user enters a username; Entra ID performs home realm discovery and offers Use a certificate or smart card. The client is redirected to the certificate authentication endpoint, certauth dot login dot microsoftonline dot com in the commercial cloud, which includes GCC, and the dot us endpoint in Azure Government. It requests the client certificate in a mutual-TLS handshake. Entra ID checks the chain and the CRL, and finds one user through the username bindings. If Conditional Access requires MFA and the certificate counts as multifactor, the user is signed in; if it's single-factor, Entra offers a registered second factor. Allow the endpoint through proxies and turn off TLS inspection for it, or the client certificate never reaches Entra ID. The trust store. Upload every CA in the chain that issues user certificates. Microsoft highly recommends the PKI-based trust store, which holds up to two hundred fifty CAs. Managing it takes Privileged Authentication Administrator, and bulk upload needs P1 or P2. The trust store is also a blast radius: adding a CA lets any certificate it issues authenticate any user it can be bound to. Revocation. Set each CA's base CRL URL, and the delta if published; without one, a revoked certificate still authenticates, so turn on Require CRL validation. Entra ID supports one CRL endpoint per CA over HTTP or HTTPS, with HTTP recommended, downloaded within ten seconds. It doesn't support OCSP. Interactive sign-in downloads CRLs up to twenty megabytes in the commercial cloud including GCC, and forty-five in Azure Government. And it caches the CRL until its next update, so revoke the user's sessions when revocation must be immediate. Workbook: Book 07, Chapter 06 — Device and User Certificates, "How a CBA sign-in works" and "The trust store."

## Slide 22: Username bindings, affinity and factors
WHAT
Affinity | Bindings to certificateUserIds
High | SKI, SHA1PublicKey, IssuerAndSerialNumber
Low | PrincipalName, RFC822Name, Subject, IssuerAndSubject
HOW ENTRA EVALUATES THEM
Priority order, lowest number first; only Graph shows it
Requiring high affinity drops every low-affinity binding
CBA is only as secure as the lowest-affinity binding: one low at most
Production requires high affinity; set it only when certificateUserIds is correct
SINGLE OR MULTIFACTOR
The authentication binding policy
Default single-factor; rules by issuer, policy OID, or both
Issuer-and-OID beats OID, OID beats issuer; mixed results count as single-factor
Multifactor only if a PIN or biometric protects the key: a PIV card, not a software certificate
A derived credential with its own OID needs its own rule
Target CBA to groups that hold certificates, never All users; keep a TAP path
CBA needs no premium license; Conditional Access needs P1
Sources: Microsoft Learn — Entra CBA technical concepts; set up Entra CBA; Entra licensing. Book 07, Ch 06; Book 03, Ch 09.
Notes: [34:30–36:30] Username bindings map a certificate field to a user attribute. By default the SAN principal name maps to the user principal name. Microsoft classes subject key identifier, SHA-1 public key, and issuer and serial number as high affinity, and principal name, email, subject, and issuer and subject as low. The old guide classed issuer plus subject as high; Microsoft classes it as low, because a CA can issue several certificates with the same subject. How Entra ID evaluates them. In priority order, lowest number first, and only Graph shows the priority. If the tenant or a custom rule requires high affinity, every low-affinity binding is dropped. So with several bindings, CBA is only as secure as the lowest-affinity one. Configure one low-affinity binding at most. The program's position: production tenants require high affinity, using issuer and serial number or SKI in certificate user IDs. Low-affinity UPN binding is acceptable in a pilot. But setting the tenant-wide requirement to high before every user's values are correct locks those users out. The authentication binding policy decides one factor or two. The default is single-factor; rules can be by issuer, by policy OID, or both. Issuer-and-OID rules beat OID rules, and OID rules beat issuer rules; a certificate whose OIDs map to both is single-factor. Microsoft says to treat a certificate as multifactor only if a PIN or biometric protects it, so a PIV card qualifies and a software certificate doesn't. Two rules prevent lockout. Target CBA to groups that hold valid certificates, never All users, and give people without a certificate another path, such as a Temporary Access Pass. CBA itself needs no premium license; Conditional Access, which every real deployment uses, needs P1. Workbook: Book 07, Chapter 06 — Device and User Certificates, "Username bindings and affinity," "Single-factor and multifactor certificates," "Conditional Access."

## Slide 23: Staged rollout, and moving off AD FS
HOW
STAGED ROLLOUT
A test mechanism, not a mixed state
Synced users only; browser and modern authentication only
Up to 10 groups per feature; no nested or dynamic groups
200 users when a group is first added; later changes take up to 24 hours
Password sign-in for CBA pilot users needs password hash sync
Separate groups for the CBA method and for staged rollout
Issue a TAP after adding a user, to skip the extra federated sign-in
FROM AD FS TO ENTRA CBA
Only the check point moves
Trust parity: every AD FS-trusted CA in the Entra store, with internet CRLs
Binding parity: claim rules become bindings; sync altSecurityIdentities
Protect the sync path: Entra Connect admins can change bound values
Keep staged rollout short: federation risk lasts until conversion
Record and back up the federation configuration first
Conversion is reversible while the AD FS farm can be restored
Sources: Microsoft Learn — Staged rollout; Migrate from federation to Entra CBA; Migrate from federation to cloud authentication. Book 07, Ch 06; Appendix A.2.
Notes: [36:30–38:27] Staged rollout lets synchronized users in a federated domain sign in at Entra ID with CBA instead of being sent to AD FS, while everyone else stays federated. Microsoft is explicit that it's a temporary testing mechanism, not a permanent mixed state, and its limits are tighter than the old guide implied. It applies only to users synced by Entra Connect, and only to browser and modern authentication; legacy authentication still goes to the federation server. Up to ten groups per feature, and no nested or dynamic groups. A group added for the first time is limited to two hundred users, and later membership changes take up to twenty-four hours. Password sign-in for CBA pilot users works only with password hash sync. And issue a Temporary Access Pass right after adding a user, so the first sign-in doesn't fall back to the federation server. The program pilots with cloud groups of ten to twenty users, confirms in the sign-in log which binding matched and what level was granted, and grows in steps until the domain converts. Moving off AD FS certificate authentication doesn't change the credential or the PKI; only the place where authentication and revocation are checked moves. Get trust parity, with internet-reachable CRLs. Get binding parity, syncing account mappings to certificate user IDs where AD FS used them, and protect that sync path. Keep staged rollout short, because staged users stay exposed to a federation server compromise until the domain converts. Record the federation configuration and back up the farm. And the old guide called conversion one-way; it isn't. Microsoft's rollback is to re-federate, which works only while AD FS can still be brought back. Workbook: Book 07, Chapter 06 — Device and User Certificates, "Staged rollout" and "Migrating from AD FS certificate authentication"; Appendix A, checklist A.2.

## Slide 24: Module 4: Coexistence, migration and retirement
Part 2 — Issuing, migrating and retiring · Chapters 07–08, Appendices A–B
Presented by Michael F. Stratton
Not an official U.S. government publication. Independent technical analysis; not reviewed or endorsed by any federal agency.
IN THIS MODULE · ABOUT 12 MINUTES
Coexistence rules, two-way trust and CRL reachability
Six gated waves and the template migration matrix
Renewal, monitoring, decommissioning and evidence
Notes: [38:27–39:14] Module 4: coexistence, migration and retirement. Coexistence isn't a phase at the end of the project; it's the condition the project runs in. From the day the first Cloud PKI certificate is issued until the last AD CS-dependent workload retires, devices carry certificates from both issuers, relying parties trust both chains, and two sets of CRLs have to stay reachable. For most of the migration, both PKIs are production. The plan has to say which one each certificate comes from on any given day, and how to go back. Then, after the migration, the work becomes keeping every certificate owned, renewed and checkable, and retiring the old CAs without stranding a single one. Workbook: Book 07, Chapter 07 — Coexistence and Migration; Chapter 08 — Lifecycle, Monitoring and Decommissioning.

## Slide 25: Coexistence: five rules and trust in both directions
HOW
THE COEXISTENCE RULES
One issuer per use case per population
Trust goes up before issuance moves
Revocation reachable wherever validation happens
Nothing is revoked to force a move
Every move has a tested rollback that doesn't depend on what it retired
Direction | How
AD CS into Entra ID | Root and every intermediate and issuing CA in the trust store, each with an internet CRL
Cloud chain into the forest | GPO trusted roots, or publish RootCA to the directory; BYOCA adds the issuing CA to the intermediate store
NTAuth | Only for CAs that issue logon certificates, and only with strongly mapped profiles
Each forest | Its own distribution and NTAuth entry; one Entra trust store
Stays on AD CS until AD retires: DC certificates from a Kerberos Authentication copy (Client, Server and KDC Authentication; HTTP CRL first for Entra-joined devices), LDAPS, and NPS and other server certificates.
Sources: Microsoft Learn — Windows Hello DC certificate guidance; Entra joined SSO; LDAPS certificates; set up Entra CBA; GPO certificate distribution; certutil -dspublish; NTAuth import. Book 07, Ch 07.
Notes: [39:14–41:17] The program's coexistence rules. Each use case has one issuer at a time per population: a device group gets its Wi-Fi certificate from AD CS or from Cloud PKI, never both by design. Trust goes up before issuance moves: a relying party trusts the new chain before the first certificate from it reaches anything that relying party sees. Revocation must be reachable wherever validation happens. Nothing is revoked to force a move: an AD CS certificate is replaced at renewal or expiry. And every move has a tested rollback that doesn't depend on something the move retired. What stays on AD CS until Active Directory retires. Domain controller certificates, because Cloud PKI doesn't issue to servers. Use a copy of the Kerberos Authentication template. Entra-joined devices can't read a CRL from AD before they authenticate, so publish an HTTP CRL listed first. LDAPS stays too; the old guide said it could move to Cloud PKI, but an LDAPS endpoint is a server. Other server certificates stay on AD CS as well, renewed through CyberArk Certificate Manager, as Chapter 04 decided. NPS needs care: it must trust the Cloud PKI chain before the first pilot device gets a cloud Wi-Fi certificate, and keep trusting AD CS until the last AD CS client certificate expires. Trust runs both ways. AD CS into Entra ID: upload the root and every intermediate and issuing CA, each with an internet-facing CRL; that's also what lets AD FS certificate authentication move without reissuing anything. The cloud chain into the forest: by Group Policy or by publishing to the directory. NTAuth only for CAs that will issue logon certificates. And each forest needs its own distribution, while every forest's user-issuing root goes into the single Entra trust store. Workbook: Book 07, Chapter 07 — Coexistence and Migration, "Two PKIs, one estate," "What stays on AD CS," "Trust in both directions."

## Slide 26: CRL availability: outages are revocation outages
WHAT
CA | Where its CRL lives | Who must reach it | Watch for
Cloud PKI root and issuing | Intune-hosted; seven days, republished every 3.5 | Every relying party, including on-premises RADIUS and VPN | Outbound HTTP from RADIUS and VPN servers to the Intune CDP and AIA
BYOCA issuing CA | Intune-hosted | As above | Parent CRL and AIA come from the private CA; AD CS defaults to LDAP AIA
AD CS CAs for CBA user certificates | Often LDAP plus an internal HTTP URL | Entra ID, over the internet: one HTTP (or HTTPS) URL per CA | Internal-only URLs; CRLs over 20 MB (commercial and GCC) or 45 MB (Azure Government)
AD CS behind DC certificates | As above | Entra-joined devices, before authentication | LDAP-only CDPs: publish an HTTP CDP first
Fixing a CDP: add an internet HTTP location; only certificates issued after the change carry it. Entra uses the URL in its trust store, so CBA works at once. Publish on plain anonymous HTTP, not an app proxy.
Sources: Microsoft Learn — Cloud PKI overview; configure BYOCA; Entra CBA CRL; set up Entra CBA; Entra joined SSO CRL requirements. Book 07, Ch 07.
Notes: [41:17–43:10] Most coexistence outages are revocation outages. Relying parties now sit in three places, inside the network, on the internet, and in Entra ID, and each CA's CRL must be reachable from all three wherever its certificates are validated. Every relying party that validates Cloud PKI certificates, including on-premises RADIUS and VPN servers, needs outbound HTTP to the Intune-hosted CDP and AIA. A BYOCA issuing CA's own CRL is Intune-hosted too, but its parent CRL and AIA come from the private CA, and AD CS defaults to an LDAP AIA location. AD CS CAs that issue user certificates for Entra CBA usually publish over LDAP plus an internal HTTP URL; Entra ID needs one internet HTTP or HTTPS URL per CA, HTTP recommended, with no OCSP and no LDAP, and watch the CRL size limits, twenty megabytes for commercial and GCC and forty-five for Azure Government. And the CAs behind domain controller certificates must serve Entra-joined devices that haven't authenticated yet, so LDAP-only distribution points break them. Fixing an AD CS distribution point means two things. Add an HTTP location reachable from the internet, using HTTP rather than HTTPS. And recognize that the new URL appears only in certificates issued after the change. Entra ID uses the CRL URL configured in its trust store, not the one inside each certificate, so CBA works as soon as the trust store points at the published CRL; other relying parties keep failing until their certificates renew. The program publishes on plain anonymous HTTP, not through an application proxy, because Entra ID must download the CRL without authentication within ten seconds. Workbook: Book 07, Chapter 07 — Coexistence and Migration, "CRL availability."

## Slide 27: Six gated waves, each with a tested rollback
HOW
Wave | Weeks | Exit gate | Rollback
1 Assess | 1–4 | Every template classified; Critical and High findings remediated and re-tested; PKI owner and security sign off | None needed: the wave reads
2 Foundation | 5–8 | Issuing CA active; trust profiles on 99% of devices; test certificate valid everywhere; CRLs reachable from all three places | Unassign trust; remove CAs from Entra; delete a Cloud PKI CA last
3 Pilot | 9–16 | 95% issuance success; CBA at the intended level; every pilot relying party accepts the chain | Remove SCEP assignments: devices fall back to AD CS certificates
4 Scale | 17–28 | Cloud certificates for every MIGRATE use case; AD CS autoenrollment removed per ring | Per ring: re-link autoenrollment, then remove SCEP
5 Cutover | 29–36 | Domains managed; AD FS certificate authentication off | Re-federate; four-hour objective while AD FS is restorable (30 days)
6 Decommission | 37–44 | MIGRATE-only components retired; root retained and documented | Restore the CA from backup: plan 8–12 hours
Removing a profile revokes: unassigning or editing a SCEP profile revokes its certificates on Windows and Apple platforms, so autoenrollment stays on until each wave's exit gate.
Sources: Microsoft Learn — remove SCEP or PKCS certificates; staged rollout; migrate from federation; AD FS decommission guide; Cloud PKI in-place renewal. Thresholds and durations are program figures. Book 07, Ch 07; App. A.
Notes: [43:10–45:06] The migration runs as six waves. Each wave's exit gate is the next one's entry gate, and each has its own rollback. The durations are program planning figures for a single-forest estate, not commitments; scale them to the wave 1 inventory. Appendix A turns each wave into a checklist with an owner and a verification per line. Wave 1, Assess, weeks one to four: inventory every CA and template, run the Chapter 03 checklist, classify every template, list every relying party, and run the strong-mapping sweep. It reads, so it needs no rollback. Wave 2, Foundation: create the Cloud PKI CAs with licensed keys, upload user-issuing CAs to the Entra trust store, deploy trust profiles and the cloud chain to domain-joined relying parties, and test. The gate is trust profiles on at least ninety-nine percent of managed devices and every CRL reachable from inside, outside and Entra. Wave 3, Pilot, fifty to a hundred devices: Wi-Fi then VPN, then CBA through staged rollout, with AD CS autoenrollment left on so the rollback works. The gate is ninety-five percent issuance success. Wave 4, Scale, in rings; remove autoenrollment for each ring once its cloud certificates are accepted. Wave 5, Cutover: record federation settings, convert domains starting with the smallest, and keep AD FS restorable for thirty days, which is what makes the four-hour recovery objective achievable. Wave 6, Decommission. The rules across waves: rehearse each rollback in a test scope first, and never let a rollback depend on a component the same wave retires. Removing or editing a SCEP profile revokes its certificates on Windows and Apple platforms, so treat profile changes as changes with impact. Workbook: Book 07, Chapter 07 — Coexistence and Migration, "Renewal while two issuers overlap," "The migration playbook," "Rollback rules"; Appendix A, checklist A.1.

## Slide 28: The template matrix: classify by what was actually issued
WHO
AD CS template | Class | Target
User; Computer and Workstation | MIGRATE (servers BRIDGE) | Cloud PKI SCEP, SID URI where used against AD
Web Server | RETAIN | AD CS or public CA, via CyberArk Certificate Manager
Kerberos Authentication; LDAPS | BRIDGE | AD CS until the last DC; the DC certificate serves LDAPS
Domain Controller (older) | BRIDGE, then superseded | A Kerberos Authentication copy
RAS and IAS Server | BRIDGE | AD CS while NPS runs, renewed via CyberArk
Exchange Signature Only | MIGRATE (delivery) | Intune PKCS profile from AD CS
Exchange User | MIGRATE (delivery); RETAIN (issuer) | Imported PKCS; the existing CA keeps issuing
Basic EFS; EFS Recovery Agent | RETIRE (agent last) | None; keep recovery keys while data remains
Enrollment Agent; OCSP Response Signing | RETIRE, conditionally | When no workflow or OCSP consumer remains
BEFORE A MIGRATE ROW MOVES
Wave 4's per-ring exit test
Every relying party trusts the new chain and reaches its CRL
The Intune profile issues at the program's threshold
Certificates used against AD are strongly mapped
Old certificates on a dated path to expiry; autoenrollment off only after that
Sources: Microsoft Learn — Cloud PKI overview; Intune platforms; PKCS profiles; certificate template concepts; Windows Hello DC certificates; LDAPS; EAP-TLS requirements; Entra CBA CRL. Book 07, Appendix B; Ch 02.
Notes: [45:06–47:20] Appendix B is the starting matrix that seeds wave 1. Classify each template by what it actually issued, not by its name. Three facts drive most rows. Cloud PKI issues only through SCEP, only to Intune-enrolled devices, and Intune doesn't manage Windows Server, so every server certificate is BRIDGE or RETAIN, never MIGRATE. And PKCS profiles move delivery to Intune, not issuance off AD CS. So: User, Computer and Workstation Authentication are MIGRATE for Intune-managed devices, to Cloud PKI SCEP, with the SID URI where the certificate is used against AD; servers stay on autoenrollment. Web Server is RETAIN, on AD CS or a public CA for internet-facing names, with lifecycle automation through CyberArk Certificate Manager. The old guide had it as MIGRATE to Cloud PKI; web servers aren't Intune devices. Kerberos Authentication and LDAPS are BRIDGE until the last domain controller; the domain controller certificate from the Kerberos Authentication copy serves LDAPS. The older Domain Controller templates lack the KDC Authentication OID, so they're superseded by a Kerberos Authentication copy. RAS and IAS Server stays while NPS runs, renewed through CyberArk Certificate Manager. Exchange Signature Only migrates delivery. Exchange User carries two verdicts: MIGRATE for delivery, because Intune delivers it, and RETAIN for the issuer, because the existing CA and its key history stay. EFS retires, but the recovery agent retires last: keep its certificates and keys until no encrypted data remains. Before any MIGRATE row moves, four things must be true, and they're wave 4's per-ring exit test. Every relying party trusts the new chain and can reach its CRL. The Intune profile issues at the program's success threshold. Certificates used against Active Directory carry a strong mapping. And the template's remaining certificates are on a dated path to expiry, with autoenrollment removed only after the profile is issuing. For BRIDGE rows, record the event that ends them, so retirement is scheduled rather than forgotten. Workbook: Book 07, Appendix B — Certificate Template Migration Matrix; Chapter 02.

## Slide 29: Renewal at scale, monitoring and drift
HOW
Renewal engine | Covers | What to watch
Intune profiles | Certificates on Intune-managed devices | Apple renews only inside the threshold, unlocked; a failed renewal isn't retried
AD CS autoenrollment | DC certificates, which also serve LDAPS | CA online and CRL current while the class exists
CyberArk Certificate Manager | Server TLS incl. NPS and RADIUS, public TLS, appliances, network devices | A Server Owner per certificate; a scoped CA account
ACME
Through the CLM platform: http-01, dns-01
ACME service: FIPS mode off
DRIFT THE PROGRAM DETECTS, AT LEAST WEEKLY
Expiring within two renewal windows with no engine bound · issuance outside policy (4887 for retired templates, NTAuth changes, unrecorded certificates)
Missing strong mapping (no SID extension or SAN URL; event 39) · a SID mismatch (event 41; 49 on 2008-era DCs) treated as a security event
Trust store drift: an unapproved anchor is an SC-17(b) finding · stale CRLs (AADSTS220501) · posture regression in Defender for Identity
Sources: CA/Browser Forum SC-081v3 and BRs; RFC 8555; CyberArk — Certificate Manager Self-Hosted and ACME docs (v26.1); Microsoft Learn — SCEP profiles; AD CS revocation; KB5014754; Entra CBA. Book 07, Ch 08.
Notes: [47:20–49:27] Migration ends on a date; certificates don't. Public TLS validity falls to forty-seven days from March 15, 2029. The schedule binds publicly trusted certificates, but the program aligns internal lifetimes with it as automation proves itself. The design rule: no certificate class may depend on a person remembering a date. The target has three renewal engines. Intune profiles renew certificates on managed devices at the profile's renewal threshold, with a new key pair for SCEP. On Apple platforms, renewal happens only inside the threshold window with the device unlocked, and a failed renewal leaves the expired certificate in place without a retry. AD CS autoenrollment renews domain controller certificates, which also serve LDAPS, so the CA must stay online and its CRL current. And CyberArk Certificate Manager discovers, tracks and renews server TLS, including NPS and RADIUS servers, appliances, public TLS and network devices, with a Server Owner on every certificate. Neither Microsoft issuer in the target offers ACME, so the program provides it through the lifecycle platform. CyberArk documents the http-01 and dns-01 challenges. One federal limit: CyberArk's installation guide says FIPS mode isn't supported for its ACME service at all, so run the ACME service on dedicated servers outside the FIPS-mode server set. The drift checks run at least weekly and are committed to the evidence repository, because an assessor asks how long a finding stayed open. Watch for certificates within two renewal windows of expiry with no engine bound, issuance outside policy, missing strong mapping, trust store anchors that aren't approved, stale CRLs, and posture regressions. And treat a SID mismatch as a security event: it can mean the certificate was issued to a different user. That's event 41 on current domain controllers, but event 49 on Server 2008 and 2008 R2, where 41 means no strong mapping. Workbook: Book 07, Chapter 08 — Lifecycle, Monitoring and Decommissioning, "Renewal at scale," "ACME where it applies," "Monitoring," "Compliance and drift detection."

## Slide 30: Retire AD CS last, and hand the assessor the evidence
WHO
GATE: CUTOVER DONE, 30 DAYS CLEAN, RETAINED CLASSES RUNNING
Confirm no dependents; stop new issuance; deny pending requests
Back up and archive the database and key, password stored separately
Revoke for cessation of operation; final CRL outlives the certificates
Remove NDES and web services before the CA; move OCSP users to CRLs
Remove the CA from Entra, Intune, GPO, NTAuth and the CLM platform
Keep CDP and AIA serving until the last certificate expires; record it
Control | What the assessor reads
IA-5(2)(a) | TPM key storage; PKCS hosts in scope; bindings, affinity and strong-mapping event counts
IA-5(2)(b) | Trust store export with a CRL per CA; Require CRL validation; CRL freshness; caching
SC-12 | Managed HSM (FIPS 140-3 Level 3); AD CS HSM keys, ceremonies, custody
SC-17(a) | Certificate policy, template inventory, 4886–4888, CLM records; Federal PKI for PIV
SC-17(b) | Entra, Intune, GPO and NTAuth anchors; trust store drift findings
Sources: Microsoft Learn — Decommission an enterprise CA (KB 889250); AD CS revocation and CDP changes; Managed HSM; NIST SP 800-53 Rev. 5 (IA-5(2), SC-12, SC-17). Book 07, Ch 08.
Notes: [49:27–51:26] Last, retiring AD CS, which is the program's sixth wave. It applies only to the CAs and role services that no longer serve a retained class; domain controller, LDAPS and RADIUS certificates usually keep at least one issuing CA alive for as long as domain controllers exist. The gate: cutover complete, the thirty-day rollback window passed with no incidents, and every retained class running on the CAs that remain. Confirm nothing depends on the CA, using the lifecycle inventory and the CA database. Stop new issuance: remove the templates, unlink autoenrollment, deny pending requests. Back up the database and key, with the backup and its password through separate channels. Revoke outstanding certificates for cessation of operation, set the CRL lifetime past the remaining certificates' lifetime, and publish. Remove NDES and the web services before the CA, and move any OCSP consumers to CRL checking. Clean up trust in Entra, Intune, Group Policy, NTAuth and the lifecycle platform. Keep the CDP and AIA endpoints serving until the last certificate expires, delete templates only after every CA in the forest is gone, and commit a decommission record. Under BYOCA, the root and any CA that signed the Cloud PKI issuing CA stay. The assessor reads NIST SP 800-53 evidence: key storage and binding settings for IA-5 enhancement two, the trust store and CRL configuration for path validation, HSM key protection for SC-12, and the certificate policy and approved trust anchors for SC-17. So, from Monday: harden first and gate on it, choose the root deliberately, issue strongly mapped certificates, run both PKIs with reachable CRLs, and retire AD CS last, with evidence. Chapters 03 through 08 and the appendices carry the detail. Thank you. Workbook: Book 07, Chapter 08 — Lifecycle, Monitoring and Decommissioning, "Decommissioning AD CS" and "The evidence an assessor reads"; Chapters 03–07; Appendices A–B.